## Slide 1: Training Course SVR800
2014/3/15
Mariame

## Slide 2: SVR 800
SVR 800 is a Network Video Recorder (NVR) made by SEEnergy Corp.
An external device that helps to monitor the IP cameras of the users.
It can display and manage simultaneously channels up to 16 and have multiple function.
SVR800

## Slide 3: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800

## Slide 4: Installation
  To connect to the NVR, use a PC that is on the same network (LAN) over a switch or hub, or connect the PC directly to the NVR using a crossover CAT5 Ethernet cable.
SVR800

## Slide 5
The NVR comes with a pre-configured static IP “192.168.101.50”. However, it is only used when there is no DHCP server presented in the network.
The NVR will turn on its DHCP server function and act as the DHCP server in the network.
Or it will get automatically an IP Address from the pre existing DHCP server.
Installation
SVR800
SVR 800 Default network configuration

## Slide 6
Install first “NVR device Search” utility software.
Then find the IP address of the SVR that matches the SVR’s MAC address on the displayed list.
How to find the IP address of the SVR?
P.S If there is no DHCP server available on the Network.
SVR’s IP address will be “192.168.101.50”
Installation
SVR800

## Slide 7
Web UI => Internet Explorer
Or
Installation
SVR800
Two ways to display the NVR’s User Interface (UI)
Local UI => Connect a Monitor directly to the NVR through VGA or HMDI port

## Slide 8: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800

## Slide 9
Access to the NVR through Web UI
  Open Internet Explorer (IE) with administrator privileges
  Type the SVR’s IP address on the address bar
  Log in with default settings:
  Username: Admin / Password: Admin
Configuration
SVR800
1
2

## Slide 10
Access to the NVR through Web UI: Main View
SVR800
Configuration
Go to settings page
Notes: After login in in the web UI, the Main view will be displayed.
Click on « Settings » to start configuration

## Slide 11: PLAN
SVR800
Installation
Configuration
Main View
Maintenance
Training Course SVR800
System Configuration
Channel Configuration
Event Configuration
Recording Configuration

## Slide 12
Network Configuration
Edit NVR’s network configuration
SVR800
Configuration

## Slide 13
Network Configuration
Choose the “Auto Mode” or “DHCP Client” if there is already a DHCP server on the LAN.
SVR800
Configuration
Notes: It has 3 types of connection : Auto Mode, DHCP Client, Static IP

## Slide 14
Network Configuration
Choose the “static IP” mode if you want to set static IP address for the NVR.
SVR800
Configuration

## Slide 15
Users Account
Default account’s username is “admin” with password “admin”.
SVR800
Configuration
Notes: Multiple users can access the recorder simultaneously. You can add, remove and edit users.
It is highly recommended to change the password upon your initial login.

## Slide 16
Users Account : Change user’s password
SVR800
Configuration
Notes: We highly recommend to change the default password of “admin” account.

## Slide 17
Users Account : Add a User
SVR800
Configuration
Notes: • Enter a username and password in “User Account Information”. All other fields are optional for your own reference.
• Select a group from the “Group” drop-down menu to assign the new user to a particular group
• Enter a short description for the account if you wish
• Click “Add” to finish configuration

## Slide 18
Users Account
View of added users to the system
SVR800
Configuration
Notes: Multiple users can access the recorder simultaneously. You can add, remove and edit users.
It is highly recommended to change the password upon your initial login.

## Slide 19
Group Privileges : Customize access policies for each group
SVR800
Configuration

## Slide 20
Group Privileges : Customize access policies for each group
7 available Groups :
Group 1 to Group 5 are customizable + Admin Group+ Guest Group
“Guest” group privilege: “view-only” privilege in the “Live View” page. Users in this group don’t have the rights to make any changes in the “Live View” page. Guest group cannot access to other pages.
User can alter settings by checking or unchecking the checkbox
Group’s Name can be changed.
SVR800
Configuration

## Slide 21
Disk setup
SVR800
Configuration
Notes: The disk setup displays the number of HDDs plugged in the NVR.

## Slide 22
Disk setup
First, install a hard disk in the SVR,
Then, Initialize it to be ready for recording => click on the “Format” button.
SVR800
P.S
Plug in the HDD when the NVR is OFF.
The external HDDs will only be listed in the "USB Backup”
Configuration

## Slide 23: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
System Configuration
Channel Configuration
Event Configuration
Recording Configuration

## Slide 24
Channel Setting: Add a channel
SVR800
Configuration

## Slide 25
Channel Setting : Add a Channel
Two options for adding a new camera :
Option1: Automatic search of the cameras by the NVR on the same LAN.
SVR800
Option2: Enter camera’s information and add it manually to the channel.
Configuration

## Slide 26
Channel Setting:
Option1 Add a camera with automatic search function
SVR800
Configuration
List of cameras available on the same LAN as the NVR.
Select the camera from the list then press « Configure »
Notes: Simply select a camera from the list and press “Configure”

## Slide 27
Channel Setting
Option1 Add a camera with automatic search function
SVR800
Type in the username and password then press « Detect » button
1
2
Configuration

## Slide 28
Channel Setting
Option2 Add manually a camera
SVR800
1
2
Configuration

## Slide 29
Channel Setting
Configure the channel
SVR800
Configuration

## Slide 30
Things to consider before setting the channel’s configuration!
The max throughput of the SVR
SVR800 max throughput: 94 Mbps <=> 16CH*30 fps at Full HD and H.264 codec
SVR800
Configuration

## Slide 31
VBR or CBR configuration
It depends on users requirements. User can either prioritise the image quality or the network’s flow stability. User needs to choose the VBR (Variable bitrate) or CBR (Constant bitrate).
SVR800
Configuration
Things to consider before setting the channel’s configuration!

## Slide 32
Channel setting
Add the camera after setting the right configuration
SVR800
Configuration
Notes: The camera is successfully added to the channel

## Slide 33
Channel Setting
Add the camera after setting the right configuration
SVR800
Configuration
The new channel appears on the list
Notes: The new channel appears on the list

## Slide 34: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
System Configuration
Channel Configuration
Event Configuration
Recording Configuration

## Slide 35
Event Configuration
General settings
SVR800
When event is triggered?
How often is the event triggered?
What to do when event is triggered?
Configuration
Notes: General Settings:
It can help :
Quickly configure when an event is triggered.
How often events are triggered
Corresponding actions when events are triggered

## Slide 36
Event Configuration:
Event Servers are used as media to send alerts when NVR is triggered.
SVR800
Motion detection
Disk Failure
SMTP server
Administrators
Configuration
Detects
Detects
Send Alerts
Send Alerts
Triggers
Triggers
FTP server

## Slide 37
Event Configuration
FTP Server Settings
SVR800
1
2
3
Configuration

## Slide 38
Event Configuration
SMTP Server Settings
SVR800
Supported authentication methods of the SMTP server:
PLAIN
LOGIN
CRAM-MD5
DiGEST-MD5
Configuration
Notes: It does not support GMAIL, Hotmail, Yahoo

## Slide 39
SVR800
Event Configuration
Event trigger
Configuration
Notes: •Which channels will have event trigger function enabled
•What is considered to be an event •Where the warnings will be sent to and how they will be sent

## Slide 40
SVR800
Event Configuration
Event trigger
Event trigger can be enabled for each Channel .
“ custom event ” option allows the NVR to receive events from the CMS software and start recording; events such as the intelligent video detection in the CMS.
Configuration
Notes: •Which channels will have event trigger function enabled ?

## Slide 41
SVR800
Event Configuration
Event trigger
Define what is considered to be an event
Define how and where the notifications will be sent
Configuration
Notes: What is considered to be an event?
Where the warnings will be sent to and how they will be sent ?

## Slide 42: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
System Configuration
Channel Configuration
Event Configuration
Recording Configuration

## Slide 43
SVR800
Recording Configuration
General Settings
Configuration

## Slide 44
SVR800
“ Pre-Alarm” time sets the NVR to record in advance when an event is triggered.
“Post-Alarm” time sets the NVR to continue recording for a period of time after an event trigger is finished.
Configuration
Recording Configuration
General Settings

## Slide 45
SVR800
Set different frame rate for different types of recording instead of recording at one frame rate only.
Configuration
Recording Configuration
General Settings

## Slide 46
SVR800
Keep the previous recording for a number of days.
If this option is enabled, once the hard drive is full, the recycle function will then start but it will ensure that the number of days of recording data defined here will stay in hard drive instead of wiping out 20GB of data at a time.
Configuration
Recording Configuration
General Settings

## Slide 47
SVR800
Define the type of recording
Enable/disable audio recording on recorded videos
Configuration
Recording Configuration
General Settings

## Slide 48
Recording Configuration
Schedule recording Settings
SVR800
Define the time range of the schedule recording for each channel
Choose a channel
Configuration a
Configuration b
or
Configuration

## Slide 49
SVR800
Define the time range of the schedule recording for each channel
Configuration a: Schedule table
P.S Each cell box represents 15 minutes of time. Click one or more boxes to omit consecutive recording.
Choose first the channel then select the prefered time slot .
Click on the time slot then slide the cursor :
    Horizontaly to choose the recording hours
    Verticaly to choose the recording days
Configuration
Recording Configuration
Schedule recording Settings

## Slide 50
SVR800
Define the time range of the schedule recording for each channel
Configuration b: Quick Configuration
Copy the configuration to all the channels or apply it to specific ones
Recording Configuration
Schedule recording Settings
Configuration

## Slide 51: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
Live View
Playback
Events

## Slide 52
Live view
Main View
Main view
SVR800
The main view provides a live streaming of each channel and several interactive functions
Notes: The selected functions will be explained in the next slides.

## Slide 53
Main view
SVR800
Date and Time display
The date and Time are defined by the user on the settings section.
User’s configuration
It displays the name of the current user. If you click on the user’s name, the context menu will display the current functions
Live view
Main View

## Slide 54
Main view
SVR800
Hardware events notification
User receives notifications if a warning sound is triggered or if the hard disk drive of the NVR failed in recording data.
Channel status
Click on the icone, a page tab will display the current status of the channels added to the NVR.
Live view
Main View
Notes: It can also display the current configuration used for the event recording or the configuration settled for the scheduled and manual recording.
The channels status page is updated as long as the NVR’s main user interface is open.

## Slide 55
SVR800
P.S. - PTZ function is available by clicking on the left button of the mouse at the channel’s live view.
-To enable Zoom function, double click on the left button of the mouse.
Main view
Live view
Video Frame
Notes: If the cursor points on one of the channels, it will show a bar on the top.
The bar displays the channel’s number and several functions.

## Slide 56
Main view
SVR800
Enable digital zoom function on the video
Snapshot function
Three continuous snapshots. Each snapshot represents a frame. 1Snapshot/Frame
Send audio sound from the microphone to the audio output of the camera.
P.SThis function can only work if the camera supports audio input/ouput function.
Live view
Camera’s Menu

## Slide 57
SVR800
Lens Control
Change the Focus and Iris settings of the camera.
Preset Point Controls
Save the current position of the camera and its preset point. It helps to avoid moving manually the camera to each desired points.
Main view
Live view
Camera’s Menu
The function is only enabled if the camera supports the function .

## Slide 58
SVR800
Change Channel
It is a shortcut to configure the channel but more advanced functions are available at the NVR settings page.
Enhancements
Set the brightness and contrast on the live view of the channel .
Main view
Live view
Camera’s Menu

## Slide 59
Live view
List View
SVR800
Displays the list of channels added to the camera
The channel’s status is defined by 3 colours:
Red: The channel is recording and the live view is available
Blue: The channel is connected and live view is available
Grey: The camera is disconnected
Channels list
Main view
Notes: List view is devided in two sections:
Channels list
Sequence function

## Slide 60
SVR800
It can display 1, 4, 9, or 16 cameras at once.
Every time you click on an “ n” pattern icon, the live video of the next “n” cameras will be displayed.
To save a name the current view.
Sequence functions
The sequence mode will automatically switch between a single or a group of cameras every a certain period of time. The period is defined by user.
Display the views already saved.
Main view
Live view
List View
Notes: You are also able to switch between saved views every certain period of time by clicking on the “start sequence function”.
If you check the box beside the name of the view, you can edit or delete the view

## Slide 61
SVR800
Main view
Live view
Local UI
Notes: The Local User Interface is very similar to Web User Interface.
Unified design is made for easy user interaction

## Slide 62: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
Live View
Playback
Events

## Slide 63
PlayBack
SVR800
Select the channels
Display playback by time chart or event
Select the day
Move the playback bar to the recorded field
Main view
Notes: The playback view displays all the videos recorded by the NVR.
You can choose the channels and display the videos by time or events.
The functions are available as long as you have configured them before on the NVR settings.

## Slide 64
PlayBack
SVR800
Zoom on a range of time
Zoom on range of time and get more details on the playback bar.
Minimize the playback range frame
Minimize the bar of the playback
Main view

## Slide 65
SVR800
Main view
PlayBack
Local UI
Notes: The Local User Interface is very similar to Web User Interface.
Unified design is made for easy user interaction

## Slide 66: PLAN
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
Live View
Playback
Events

## Slide 67
Event view
SVR800
Select the channel or display all of them.
Motion detection triggered on CH3
Click on the picture to display the event video
Or
Click on event from the list
Main view
Notes: The events can only be detected and displayed if you have configured it on the NVR’s settings.
You can display the event of all the channels at once or by each channel.

## Slide 68
SVR800
Main view
Event view
Playbar for video display
Notes: Each event can be displayed.

## Slide 69
SVR800
Main view
Event view
Local UI
Notes: The Local User Interface is very similar to Web User Interface.
Unified design is made for user’s convenience.

## Slide 70
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
General Information
System Logs
Maintenance
Disk Status
PLAN

## Slide 71
Device Information
System Options
SVR800
General information
NVR’s status
Firmware version and system time
Network settings

## Slide 72
System Logs
SVR800
Posts events that are logged and recorded by the NVR’s OS.
Basic information for troubleshooting
System Options
System Logs contains events that are logged by the NVR’s system.
It provides basic information for troubleshooting.

## Slide 73
Maintenance
SVR800
System Options

## Slide 74
Maintenance
SVR800
System Options

## Slide 75
Maintenance
SVR800
Several functions available on maintenance page
Restart the NVR
Restart a camera by selecting a channel
Upgrade NVR’s Firware
Backup NVR’s Setting
Restore NVR’s Setting
Reset the NVR to Factory default
Replace NVR web UI Logo
System Options

## Slide 76
SVR800
Maintenance
Firmware Upgrade
The firmware can be upgraded through web UI .
The firmware’s file extension is “tar.gz”.
Please use the file as it is. Don’t unzip it.
P.S. Before upgrading firmware, please backup configuration in advance.
Step 1
Step2
System Options

## Slide 77
SVR800
Disk Status
It displays detailed information about the HDD which is currently installed in the NVR.
System Options

## Slide 78: PLAN Review
SVR800
Installation
Configuration
Main View
System Options
Training Course SVR800
Notes: We have completed the training

## Slide 79: Thank you for your attention !
We welcome your questions and comments.